	Asynchronous motor
in palette

in diagram
The unit implements the mathematical representation of asynchronous motor (AM). / Both three-phase and two-phase asynchronous electric motors are applicable in automatic control systems. Three-phase AM are motors designed for industrial application, while two-phase AM are special motors commonly referred to as asynchronous servomotors (ASM). / Design diagram and differential equations / Both two-phase and three-phase AM are commonly described via a system of differential equations in a fixed system of coordinates %alpha_c , %beta_c . Meanwhile three-phase motors are reduced to two-phase ones. AM design diagram is shown in Figures 1 and 2: / Figure 1 / Figure 2 / System of AM differential equations for a fixed system of coordinates connected to the stator and for a rotating system of coordinates connected to the rotor appears as follows: / left lbrace stack { U_{%alpha c}(t) = r_1 cdot i_{%alpha c}(t) + {d %PSI_{%alpha c} (t)} over {dt} , # U_{%beta c}(t) = r_1 cdot i_{%beta c}(t) + {d %PSI_{%beta c} (t)} over {dt} , # 0 = r_2 cdot i_{%alpha p}(t) + {d %PSI_{%alpha p} (t)} over {dt} - %omega_1 cdot %PSI_{%beta p} (t) , # 0 = r_2 cdot i_{%beta p}(t) + {d %PSI_{%beta p} (t)} over {dt} - %omega_1 cdot %PSI_{%alpha p} (t) ; } right none (1) / where r_1 , ~r_2 are for active resistors of rotor and stator windings; / %PSI_{%alpha c}(t) , ~ %PSI_{%beta c}(t) , ~ %PSI_{%alpha p}(t) , ~ %PSI_{%beta p}(t) are for stator and rotor flux-linkages along axes %alpha and, %beta correspondingly. / Rotational EMF to be inputted in the equation of rotor windings, will be determined as / left lbrace stack { e_{%beta p} =%OMEGA_1 cdot p_п cdot %PSI_{%alpha p} = %omega_1 cdot %PSI_{%alpha p} , # e_{%alpha p}=-%OMEGA_1 cdot p_п cdot %PSI_{%beta p} = - %omega_1 cdot %PSI_{%beta p} ; } right none (2) / where %OMEGA_1 is for rotor speed, p_п is for number of pairs of poles, %omega_1 is for electromagnetic field rotation speed (power voltage frequency), %OMEGA_1 = {%omega_1} over {p_п} . / Flux-linkages of motor windings are equal to: / left lbrace stack { %PSI_{%alpha c}(t) = L_1 cdot i_{%alpha c}(t) + L_m cdot i_{%alpha p}(t) , # %PSI_{%beta c}(t) = L_1 cdot i_{%beta c}(t) + L_m cdot i_{%beta p}(t) , # %PSI_{%alpha p}(t) = L_m cdot i_{%alpha c}(t) + L_2 cdot i_{%alpha p}(t) , # %PSI_{%beta p}(t) = L_m cdot i_{%beta c}(t) + L_2 cdot i_{%beta p}(t) , } right none (3) / where L_1 , ~L_2 are for coefficients of self-induction of stator and rotor windings, L_m is for coefficient of mutual induction between stator and rotor circuits in case their axes are aligned. / When solving the system of linear equations (3), we obtain: / left lbrace stack { i_{%alpha c}(t) ~=~ {%PSI_{%alpha c}(t) cdot L_2 ~-~ %PSI_{%alpha p}(t) cdot L_m} over {L_1 cdot L_2 ~-~ L_m^2}, # i_{%beta c}(t) ~=~ {%PSI_{%beta c}(t) cdot L_2 ~-~ %PSI_{%beta p}(t) cdot L_m} over {L_1 cdot L_2 ~-~ L_m^2}, # i_{%alpha p}(t) ~=~ {%PSI_{%alpha p}(t) cdot L_1 ~-~ %PSI_{%alpha c}(t) cdot L_m} over {L_1 cdot L_2 ~-~ L_m^2}, # i_{%beta p}(t) ~=~ {%PSI_{%beta p}(t) cdot L_1 ~-~ %PSI_{%beta c}(t) cdot L_m} over {L_1 cdot L_2 ~-~ L_m^2}, } right none (4) / Moment balance equation: / M(t) ~=~ M_ex(t) ~+~J_{%SIGMA} cdot {{d %OMEGA} over {dt}} (5) / %OMEGA(t) ~ =~ %OMEGA_1(t) cdot (1-s) ~=~ {{%omega_1(t)} over {p_п}} cdot (1-s) (6) / s is for slip coefficient for rotor speed vector relative to vector of rotating magnetic field. / When being recorded via flux-linkages and currents, electromagnetic torque for two-phase AM is equal to: / M(t) = p_п cdot left ( {%PSI_{%alpha c}(t) cdot i_{%beta c}(t) ~-~ %PSI_{%beta c}(t) cdot i_{%alpha c}(t)} right ) (7) / Electromagnetic torque for three-phase AM is equal to / M(t) = {3 over 2} cdot p_п cdot left ( {%PSI_{%alpha c}(t) cdot i_{%beta c}(t) ~-~ %PSI_{%beta c}(t) cdot i_{%alpha c}(t)} right ) (8) / State equation of asynchronous motor / Resultant magnetic flux generated by any winding of a generalized motor is commonly subdivided into main magnetic flux and leakage flux, e. g., a flux generated by the stator winding is equal to Ф_1 ~=~ Ф_10 ~+~ Ф_{1 %sigma} , where Ф_10 is for main magnetic flux, Ф_{1 %sigma} is for leakage flux. Thus, inductances of windings can be divided into main and leakage inductances: / L_1 ~=~ L_10 ~+~ L_{1 %sigma} , ~L_2' ~=~ L_20' ~+~ L_{2 %sigma}' (9) / and inductive resistances: / x_1 ~=~ %omega_1 cdot L_1 , ~ x_{1 %sigma} ~=~ %omega_1 cdot L_{1 %sigma },~ x_2' ~=~ %omega_1 cdot L_2' , ~ x_{2 %sigma}'~=~ %omega_1 cdot L_{2 %sigma }' / Let us introduce an equation: / L_10 ~=~ L_20 ' ~=~ L_{12}' ~=~ L_{21}' ~=~ L_m or x_10 ~=~ x_20 ' ~=~ x_{12}' ~=~ x_{21}' ~=~ x_m / where L_m is for magnetizing circuit inductance; / x_m is for inductive resistance of magnetizing circuit; / L_{1 %sigma} is for stator winding leakage inductance; / L_{2 %sigma}' is for reduced rotor winding leakage inductance; / L_{10} = L_m is for stator winding main flux inductance; / L_{10} = L_m is for reduced rotor winding main flux inductance; / L_{12}' = L_{21}' = L_m are for reduced mutual inductances of windings. / Let us record the system of AM equations (1) – (7) in the Cauchy form, meanwhile replacing winding currents via functions of flux-linkages and winding inductances via main and leakage inductances. Using the system of equations (3) we detect that: / left lbrace stack { i_{%alpha c}(t) ~=~ {%PSI_{%alpha c}(t) cdot (L_{2 %sigma}+L_m) ~-~ %PSI_{%alpha p}(t) cdot L_m} over {L_{1 %sigma} cdot L_{2 %sigma} + L_{1 %sigma} cdot L_{m} + L_{2 %sigma} cdot L_{m}}, # i_{%beta c}(t) ~=~ {%PSI_{%beta c}(t) cdot (L_{2 %sigma}+L_m) ~-~ %PSI_{%beta p}(t) cdot L_m} over {L_{1 %sigma} cdot L_{2 %sigma} + L_{1 %sigma} cdot L_{m} + L_{2 %sigma} cdot L_{m}}, # i_{%alpha p}(t) ~=~ {%PSI_{%alpha p}(t) cdot (L_{1 %sigma}+L_m) ~-~ %PSI_{%alpha c}(t) cdot L_m} over {L_{1 %sigma} cdot L_{2 %sigma} + L_{1 %sigma} cdot L_{m} + L_{2 %sigma} cdot L_{m}}, # i_{%beta p}(t) ~=~ {%PSI_{%beta p}(t) cdot (L_{1 %sigma}+L_m) ~-~ %PSI_{%beta c}(t) cdot L_m} over {L_{1 %sigma} cdot L_{2 %sigma} + L_{1 %sigma} cdot L_{m} + L_{2 %sigma} cdot L_{m}}, } right none (10) / While replacing currents in the formula (7) we obtain / M(t) = {1 over 2} cdot p_п cdot p_f cdot left ( {%PSI_{%alpha c}(t) cdot i_{%beta c}(t) ~-~ %PSI_{%beta c}(t) cdot i_{%alpha c}(t)} right ) (11) / where p_f is for a number of power voltage phases. / Now let us insert obtained current and moment values in equations (1) and (4), indicating , we D={L_{1 %sigma} cdot L_{2 %sigma} + L_{1 %sigma} cdot L_{m} + L_{2 %sigma} cdot L_{m}} have / left lbrace stack { {d %PSI_{%alpha c} (t)} over {dt} ~=~ U_{%alpha c}(t) ~-~ {r_1 cdot (L_{2 %sigma}(t) ~+~ L_m)} over D cdot {%PSI_{%alpha c} (t)} ~+~ {r_1 cdot L_m} over D cdot {%PSI_{%alpha p} (t)} , # {d %PSI_{%beta c} (t)} over {dt} ~=~ U_{%beta c}(t) ~-~ {r_1 cdot (L_{2 %sigma}(t) ~+~ L_m)} over D cdot {%PSI_{%beta c} (t)} ~+~ {r_1 cdot L_m} over D cdot {%PSI_{%beta p} (t)} , # {d %PSI_{%alpha p} (t)} over {dt} ~=~ ~-~ {r_2 cdot (L_{1 %sigma}(t) ~+~ L_m)} over D cdot {%PSI_{%alpha p} (t)} ~+~ {r_2 cdot L_m} over D cdot {%PSI_{%alpha c} (t)} - %omega_1 cdot %PSI_{%beta p}(t), # {d %PSI_{%beta p} (t)} over {dt} ~=~ ~-~ {r_2 cdot (L_{1 %sigma}(t) ~+~ L_m)} over D cdot {%PSI_{%beta p} (t)} ~+~ {r_2 cdot L_m} over D cdot {%PSI_{%beta c} (t)} - %omega_1 cdot %PSI_{%alpha p}(t), # {d %OMEGA(t)} over dt ~=~ {p_п cdot L_m} over {J_%SIGMA cdot D} cdot left [ {%PSI_{%beta c}(t)} cdot {%PSI_{%alpha p}(t)} ~-~ {%PSI_{%alpha c}(t)} cdot {%PSI_{%beta p}(t)} right ] ~-~ {M_возм(t)} over {J_{%SIGMA}} ,# {d %theta (t)} over dt = %OMEGA(t) . } right none (12) / Equations (12) can be considered as state equations for AM. Projections of flux-linkages on orthogonal axes, angular rotor speed and rotor rotation angle constitute the state variables hereby. Stator voltages (constituting the control vector) and moment of resistance forces are the external actions applied on the motor. / The unit has 3 input and 3 output signals. / Input signals: / 1) Stator winding voltage U_{%alpha c}(t) in a fixed system of coordinates, V. / 2) Stator winding voltage U_{%beta c}(t) in a fixed system of coordinates, V. / 3) Exciting moment M_ex(t) , N·m. / Output signals: / 1) Shaft angle q(t) , rad. / 2) Rotation angular speed (frequency) q'(t) , rad/s. / 3) Electromechanical moment on the motor rotor shaft T_e(t) , N·m; / The following can be additionally applied to the third output: / Stator winding current i_{%alpha c}(t) , А. / Stator winding current i_{%beta c}(t) , А. / Properties: / Stator circuit resistance R_1 , Ohm; / Rotor circuit resistance R_2 , Ohm; / Stator circuit inductance L_1 , H; / Rotor circuit inductance L_2 , H; / Mutual inductance L_m , H; / Moment of inertia reduced to the rotor shaft J_{%SIGMA} , kg∙m2. / Number of poles p_п , pcs. / Number of power voltage phases p_f , pcs. / Initial angle of rotor rotation q(0) , rad. / Initial speed of rotor rotation q'(0) , rad/s. / Initial flux-linkage in stator winding q, V∙s. / Initial flux-linkage in rotor winding q, V∙s. / Initial flux-linkage in stator winding d, V∙s. / Initial flux-linkage in rotor winding d, V∙s. / Additional output.