	Synchronous motor without damper windings
in palette

in diagram
The unit implements the model of permanent magnet synchronous motor without damper windings (SM). / SM Design diagram and differential equations / SM design diagram is equivalent to asynchronous motor diagram plus excitation winding circuit along axis %alpha fed with voltage U_{%alpha f p}(t) . Balance equations for SM winding voltages appear as follows (on assumption that the stator is rotated with a speed inverse to rotor speed, and the rotor is fixed): / left lbrace stack { U_{%alpha c}(t) = R_c cdot i_{%alpha c}(t) + {d %PSI_{%alpha c} (t)} over {dt} + p_п cdot %OMEGA(t) cdot %PSI_{%beta c}(t), # U_{%beta c}(t) = R_c cdot i_{%beta c}(t) + {d %PSI_{%beta c} (t)} over {dt} - p_п cdot %OMEGA(t) cdot %PSI_{%alpha c}(t), # U_{%alpha f p}(t) = R_{%alpha p} cdot i_{%alpha p}(t) + {d %PSI_{%alpha p} (t)} over {dt}, # 0 = R_{%alpha p} cdot i_{%alpha p}(t) + {d %PSI_{%alpha p} (t)} over {dt} , # 0 = R_{%beta p} cdot i_{%beta p}(t) + {d %PSI_{%beta p} (t)} over {dt} ; } right none (1) / Balance equation for moments appears as follows: / left lbrace stack { M(t) = M_e(t) + J_{%SIGMA} cdot {{d %OMEGA(t)} over {dt}}, # M_e(t) = {{p_п cdot p_f} over {2}} cdot left [ %PSI_{%alpha c}(t) cdot i_{%beta c}(t) - %PSI_{%beta c}(t) cdot i_{%alpha c}(t) right ] ; } right none (2) / In these equations: R_{c},~ R_{f},~ R_{%alpha p},~ R_{%beta p} are for ohmic resistances of stator windings, excitation windings, starting (damper) winding circuit; / i_{%alpha c}(t),~ i_{%beta c}(t),~ i_{%alpha f p}(t),~ i_{%alpha p}(t),~ i_{%beta p}(t) are for stator and rotor winding currents; / %PSI_{%alpha c}(t),~ %PSI_{%beta c}(t),~ %PSI_{%alpha f p}(t),~ %PSI_{%alpha p}(t),~ %PSI_{%beta p}(t) are for stator and rotor winding flux-linkages; %OMEGA(t) is for rotor speed; p_п is for a number of pairs of poles; p_f is for a number of power voltage phases; %omega = p_п cdot %OMEGA(t) is for magnetic field rotating speed, T_e(t) is for electromagnetic torque. / alignl left lbrace stack { %PSI_{%alpha c}(t) = L_{%alpha c} cdot i_{%alpha c}(t) + L_{%alpha m} cdot left ( i_{%alpha f p}(t) + i_{%alpha p}(t) right ), # %PSI_{%beta c}(t) = L_{%beta c} cdot i_{%beta c}(t) + L_{%beta m} cdot i_{%beta p}(t) , # %PSI_{%alpha f p}(t) = L_{%alpha f p} cdot i_{%alpha f p}(t) + L_{%alpha m} cdot left ( i_{%alpha f p}(t) + i_{%alpha p}(t) right ), # %PSI_{%alpha p}(t) = L_{%alpha p} cdot i_{%alpha p}(t) + L_{%alpha m} cdot left ( i_{%alpha f p}(t) + i_{%alpha c}(t) right ), # %PSI_{%beta p}(t) = L_{%beta p} cdot i_{%beta p}(t) + L_{%beta m} cdot i_{%beta c}(t), } right none (3) / where L_{%alpha c},~ L_{%beta c},~ L_{%alpha f p},~ L_{%alpha p},~ L_{%beta p} are for own inductances of stator and rotor circuits,are L_{%alpha m},~ L_{%beta m} for mutual inductances between windings laying along longitudinal or transversal axes. (In this system of equations symbols ' (accent) are omitted in values of rotor parameters reduced to the stator). / Let us record expressions for flux-linkages via main fluxes and leakage fluxes, i. e.: / alignl left lbrace stack { %PSI_{%alpha c}(t) = %PSI_{%alpha m}(t) + %PSI_{%alpha c %sigma}(t), # %PSI_{%beta c}(t) = %PSI_{%beta m}(t) + %PSI_{%beta c %sigma}(t), # %PSI_{%alpha f p}(t) = %PSI_{%alpha m}(t) + %PSI_{%alpha f p %sigma}(t), # %PSI_{%alpha p}(t) = %PSI_{%alpha m}(t) + %PSI_{%alpha p %sigma}(t), # %PSI_{%beta p}(t) = %PSI_{%beta m}(t) + %PSI_{%beta p %sigma}(t), } right none (4) / We obtain: / alignl left lbrace stack { %PSI_{%alpha c}(t) = L_{%alpha c} cdot i_{%alpha c}(t) + L_{%alpha m} cdot left ( i_{%alpha f p}(t) + i_{%alpha p}(t) + i_{%alpha c}(t) right ), # %PSI_{%beta c}(t) = L_{%beta c} cdot i_{%beta c}(t) + L_{%beta m} cdot left ( i_{%beta p}(t) + i_{%beta c}(t) right ), # %PSI_{%alpha f p}(t) = L_{%alpha f p} cdot i_{%alpha f p}(t) + L_{%alpha m} cdot left ( i_{%alpha f p}(t) + i_{%alpha p}(t) + i_{%alpha c}(t) right ), # %PSI_{%alpha p}(t) = L_{%alpha p} cdot i_{%alpha p}(t) + L_{%alpha m} cdot left ( i_{%alpha f p}(t) + i_{%alpha c}(t) + i_{%alpha p}(t) right ), # %PSI_{%beta p}(t) = L_{%beta p} cdot i_{%beta p}(t) + L_{%beta m} cdot left ( i_{%beta c}(t)+ i_{%beta p}(t) right ), } right none (5) / In this case the substitution diagram for motor electric part appears as follows: / Figure 1 / Let us group 1,3,4 and 2,5 of equation of system (5). We have the equations / alignl left lbrace stack { %PSI_{%alpha c}(t) = L_{%alpha c} cdot i_{%alpha c}(t) + L_{%alpha m} cdot left ( i_{%alpha f p}(t) + i_{%alpha p}(t) + i_{%alpha c}(t) right ), # %PSI_{%alpha f p}(t) = L_{%alpha f p} cdot i_{%alpha f p}(t) + L_{%alpha m} cdot left ( i_{%alpha f p}(t) + i_{%alpha p}(t) + i_{%alpha c}(t) right ), # %PSI_{%alpha p}(t) = L_{%alpha p} cdot i_{%alpha p}(t) + L_{%alpha m} cdot left ( i_{%alpha f p}(t) + i_{%alpha c}(t) + i_{%alpha p}(t) right ), # %PSI_{%beta c}(t) = L_{%beta c} cdot i_{%beta c}(t) + L_{%beta m} cdot left ( i_{%beta p}(t) + i_{%beta c}(t) right ), # %PSI_{%beta p}(t) = L_{%beta p} cdot i_{%beta p}(t) + L_{%beta m} cdot left ( i_{%beta c}(t)+ i_{%beta p}(t) right ), } right none / Or, if matrices and vectors are introduced / A_{%alpha} ~=~ left [ stack{ alignl L_{%alpha c %sigma} + L_{%alpha m}~~~~~~~ L_{%alpha m} ~~~~~~~~~~ L_{%alpha m} # alignl L_{%alpha m}~~~~~~~~~~ L_{%alpha f p} + L_{%alpha m} ~~~~~~~ L_{%alpha m} # alignl L_{%alpha m}~~~~~~~~~~~~~~ L_{%alpha m} ~~~~~~ L_{%alpha p %sigma} + L_{%alpha m} } right ] / A_{%beta} ~=~ left [ stack{ alignl L_{%beta c} + L_{%beta m}~~~~~~~ L_{%beta m} # alignl L_{%beta m}~~~~~~~~~~ L_{%beta p} + L_{%beta m} } right ] / r_{%alpha} ~=~ left [ alignl R_{%alpha c} ~~~ R_{%alpha f p} ~~~ R_{%alpha p} right ] ^ T / r_{%beta} ~=~ left [ alignl %PSI_{%beta c} ~~~ %PSI_{%beta p} right ] ^ T / i_{%alpha} ~=~ left [ alignl i_{%alpha c} ~~~ i_{%alpha f p} ~~~ i_{%alpha p} right ] ^ T / i_{%beta} ~=~ left [ alignl i_{%beta c} ~~~ i_{%beta p} right ] ^ T we obtain / i_{%alpha} ~=~ A_{%alpha} ^ {-1} cdot r_{%alpha},~ i_{%beta} ~=~ A_{%beta} ^ {-1} cdot r_{%beta} (6) / axes / axes

We have as a result
K_{%alpha} = A_{%alpha}^-1 D_{%alpha} = left [ stack{ alignl (L_{%alpha p} + L_{%alpha m}) cdot L_{%alpha f p} + L_{a m} cdot L_{%alpha p} ~~~~~ -L_{%alpha m} cdot L_{%alpha p} ~~~~~~~~~~~~~~ -L_{%alpha f p} cdot L_{%alpha m} # alignl -L_{%alpha m} cdot L_{%alpha p} ~~~~~~~~~~~~~~~ (L_{%alpha p} + L_{%alpha m}) cdot L_{c} + L_{a m} cdot L_{%alpha p} ~~~~~~~ -L_{%alpha c} cdot L_{%alpha m} # alignl -L_{%alpha f p} cdot L_{%alpha m} ~~~~~~~~~~~~~~~~~~ -L_{c} cdot L_{%alpha m} ~~~~~~ (L_{с} + L_{%alpha m}) cdot L_{%alpha f p} + L_{c} cdot L_{%alpha m} } right ] (7)
K_{%beta} = A_{%beta}^-1 D_{%beta} = left [ stack{ alignl L_{%beta p} + L_{%beta m} ~~~~~~ -L_{%beta m} # alignl -L_{%beta m} ~~~~~~ L_{%beta c} + L_{%beta m} } right ] (8)
and can write as follows:
left lbrace stack { i_{%alpha} ~=~ A_{%alpha} ^ {-1} cdot r_{%alpha} ~=~ {K_{%alpha} r_{%alpha}} over D_{%alpha},~# i_{%beta} ~=~ A_{%beta} ^ {-1} cdot r_{%beta} ~=~ {K_{%beta} r_{%beta}} over D_{%beta}, } right none (9)
where D_{%alpha} ~=~ det left (A_{%alpha} right ), newline D_{%beta} ~=~ det left (A_{%beta} right ).
On excluding currents in the initial system of differential equations (1) and introducing the symbols:
K_{11} ~=~ {R_{c} cdot K_{%alpha} (1,1)} over {D_{%alpha}},~ K_{12} ~=~ {R_{c} cdot K_{%alpha} (1,2)} over {D_{%alpha}},~ K_{13} ~=~ {R_{c} cdot K_{%alpha} (1,3)} over {D_{%alpha}}~~~~,~ newline K_{21} ~=~ {R_{c} cdot K_{%beta} (1,1)} over {D_{%beta}},~ K_{22} ~=~ {R_{c} cdot K_{%beta} (1,2)} over {D_{%beta}}~ ~~~~~~~~~~~~~~~~~~~~~~~~~~, newline K_{31} ~=~ {R_{f} cdot K_{%alpha} (2,1)} over {D_{%alpha}},~ K_{32} ~=~ {R_{f} cdot K_{%alpha} (2,2)} over {D_{%alpha}},~ K_{33} ~=~ {R_{f} cdot K_{%alpha} (2,3)} over {D_{%alpha}}~~,~ newline K_{41} ~=~ {R_{%alpha p} cdot K_{%alpha} (3,1)} over {D_{%alpha}},~ K_{42} ~=~ {R_{%alpha p} cdot K_{%alpha} (3,2)} over {D_{%alpha}},~ K_{43} ~=~ {R_{%alpha p} cdot K_{%alpha} (3,3)} over {D_{%alpha}},~ newline K_{51} ~=~ {R_{%beta p} cdot K_{%beta} (2,1)} over {D_{%beta}},~ K_{52} ~=~ {R_{%beta p} cdot K_{%beta} (2,2)} over {D_{%beta}}~ ~~~~~~~~~~~~~~~~~~~~~~~,
we obtain a system of five differential equations of the first order, which describes electromagnetic processes in synchronous motor:
left lbrace stack { {d %PSI_{%alpha c} (t)} over {dt} = U_{%alpha c}(t) - K_11 cdot {%PSI_{%alpha c} (t)} - K_12 cdot {%PSI_{%alpha f p} (t)} - K_13 cdot {%PSI_{%alpha p} (t)} - %omega(t) cdot {%PSI_{%beta c} (t)}, # {d %PSI_{%beta c} (t)} over {dt} = U_{%beta c}(t) - K_21 cdot {%PSI_{%beta c} (t)} - K_22 cdot {%PSI_{%beta p} (t)} - %omega(t) cdot {%PSI_{%alpha c} (t)}, # {d %PSI_{%alpha f p} (t)} over {dt} = U_{%alpha f p}(t) - K_31 cdot {%PSI_{%alpha c} (t)} - K_32 cdot {%PSI_{%alpha f p} (t)} - K_33 cdot %PSI_{%alpha p}(t), # {d %PSI_{%alpha p} (t)} over {dt} = - K_41 cdot {%PSI_{%alpha c} (t)} - K_42 cdot {%PSI_{%alpha f p} (t)} - K_43 cdot %PSI_{%alpha p}(t), # {d %PSI_{%beta p} (t)} over {dt} = - K_51 cdot {%PSI_{%beta c} (t)} - K_52 cdot {%PSI_{%beta p} (t)} , } right none (10)
Equations describing mechanical processes in motor
Let us calculate currents i_{%alpha c}(t),~ i_{%beta c}(t) and introduce symbols:
C_{1} ~=~ {K_{%alpha} (1,1)} over {D_{%alpha}},~ C_{2} ~=~ {K_{%alpha} (1,2)} over {D_{%alpha}},~ C_{3} ~=~ {K_{%alpha} (1,3)} over {D_{%alpha}},~ newline C_{4} ~=~ {K_{%beta} (1,1)} over {D_{%beta}},~ C_{5} ~=~ {K_{%beta} (1,2)} over {D_{%beta}}
Thus, we have:
alignl left lbrace stack { i_{%alpha c} ~=~ C_1 cdot %PSI_{%alpha c}(t) + C_2 cdot %PSI_{%alpha f p}(t) + C_3 cdot %PSI_{%alpha p}(t),~# i_{%beta c} ~=~ C_4 cdot %PSI_{%beta c}(t) + C_5 cdot %PSI_{%beta p}(t)~ } right none (12)
left lbrace stack { M(t) = M_e(t) + J_{%SIGMA} cdot {{d %OMEGA(t)} over {dt}}, # M_e(t) = {{p_п cdot p_f} over {2}} cdot left [ %PSI_{%alpha c}(t) cdot i_{%beta c}(t) - %PSI_{%beta c}(t) cdot i_{%alpha c}(t) right ] ; } right none (13)
left lbrace stack { {d %OMEGA(t)} over {dt} = 1 over J cdot left ( M_е(t) - M_ex(t) right ), # {d %theta(t)} over {dt} = %OMEGA(t), } right none (14)
where J is for moment of inertia reduced to the motor shaft, %theta(t) is for motor shaft rotation angle, M_e(t) is for electromagnetic torque, M_ex(t) is for exciting moment.
Dynamic equation for permanent magnet synchronous motor without damper windings
Thus, the dynamic equation for permanent magnet synchronous motor without damper windings is as follows:
left lbrace stack { {di_{%alpha c}(t)} over {dt} = {1 over L_{%alpha c}} cdot U_{%alpha c}(t) - {R} over {L_{%alpha c}} cdot i_{%alpha c}(t) + L_{%beta c} over {L_{%alpha c}} cdot p_п cdot %OMEGA(t) cdot i_{%beta c}(t), # {di_{%beta c}(t)} over {dt} = {1 over L_{%beta c}} cdot U_{%beta c}(t) - {R} over {L_{%beta c}} cdot i_{%beta c}(t) + L_{%alpha c} over {L_{%beta c}} cdot p_п cdot %OMEGA(t) cdot i_{%alpha c}(t) - {%lambda cdot p_п cdot %OMEGA(t)} over {L_{%beta c}}, # T_e(t) = 0.5 cdot p_п cdot p_f cdot left ( %lambda cdot i_{%beta c}(t) + (L_{%alpha c} - L_{%beta c}) cdot i_{%alpha c}(t) cdot i_{%beta c}(t) right ), # {d %OMEGA(t)} over {dt} = 1 over J cdot left ( T_е(t) - M_в(t) right ), # {d %theta(t)} over {dt} = %OMEGA(t), } right none (15)
In accordance with equations (15) stator currents i_{%alpha c}(t),~ i_{%beta c}(t) , angular rotor speed %OMEGA(t) and rotor rotation angle %theta(t) are variables of SM state. Stator winding voltage and exciting moment are input parameters.
The unit has 3 input and 3 output signals.
Input signals:
1. Stator winding voltage U_{a c} (t) in a fixed system of coordinates, V.
2. Stator winding voltage U_{b c}(t) in a fixed system of coordinates, V.
3. Exciting moment M_ex(t) , N·m.
Output signals:
1. Rotor angle q(t) , rad.
2. Rotation angular speed q'(t) , rad/s.
3. Electromechanical moment on the motor rotor shaft T_e(t) , N·m.
The following can be additionally applied to the third output:
1. Stator winding current i_{%alpha c}(t) , А.
2. Stator winding current i_{%beta c}(t) , А.
Properties:
- Stator circuit resistance, R , Ohm;
- Inductance of stator d-windings i_{%alpha c}(t) , H;
- Inductance of stator q-windings L_{%beta}(t) , H;
- Magnetic flux from permanent magnet via stator windings I, Wb;
- Moment of inertia reduced to the rotor shaft J , kg·m2;
- Number of poles p_п , pcs.;
- Number of power voltage phases p_f , pcs.;
- Initial angle of rotor rotation q(0) , rad.
- Initial rotor speed q'(0) , rad/s
- Initial stator winding d current i_{%alpha}(0) , A
- Initial stator winding q current , i_{%beta}(0) A
- Additional output.
Notes:
1) Indexes d and q correspond to axes %alpha and %beta .
2) Stator winding voltages U_{%alpha c} (t) and U_{%beta c}(t) are voltages in a rotating system of coordinates. To obtain these values from input voltages U_{a c} (t) and U_{b c} (t) the following relation is used:
left lbrace stack { {U_{%alpha c}(t)} = {U_{a c}(t)} cdot sin left ( p_п cdot %OMEGA(t) right ) - {U_{b c}(t)} cdot cos left ( p_п cdot %OMEGA(t) right ) , # {U_{%beta c}(t)} = {U_{a c}(t)} cdot cos left ( p_п cdot %OMEGA(t) right ) - {U_{b c}(t)} cdot sin left ( p_п cdot %OMEGA(t) right ) . } right none