	Synchronous motor with damper windings
in palette

in diagram
The unit implements the model of permanent magnet synchronous motor with damper windings (SMW). / SMW design diagram and differential equations / SMW design diagram is equivalent to the diagram of synchronous motor without damper windings. / The dynamic equations for electromagnetic processes: / left lbrace stack { U_{%alpha c}(t) = R_c cdot i_{%alpha c}(t) + {d %PSI_{%alpha c} (t)} over {dt} + p_п cdot %OMEGA(t) cdot %PSI_{%beta c}(t), # U_{%beta c}(t) = R_c cdot i_{%beta c}(t) + {d %PSI_{%beta c} (t)} over {dt} - p_п cdot %OMEGA(t) cdot %PSI_{%alpha c}(t), # 0 = R_{%alpha p} cdot i_{%alpha p}(t) + {d %PSI_{%alpha p} (t)} over {dt} , # 0 = R_{%beta p} cdot i_{%beta p}(t) + {d %PSI_{%beta p} (t)} over {dt} ; } right none (1) / Dynamics of mechanical processes (balance equation for moments): / left lbrace stack { M(t) = M_e(t) + J_{%SIGMA} cdot {{d %OMEGA(t)} over {dt}}, # M_e(t) = {{p_п cdot p_f} over {2}} cdot left [ %PSI_{%alpha c}(t) cdot i_{%beta c}(t) - %PSI_{%beta c}(t) cdot i_{%alpha c}(t) right ] ; } right none (2) / expressions for flux-linkages: / ( alignl left lbrace stack { %PSI_{%alpha c}(t) = L_{%alpha c} cdot i_{%alpha c}(t) + L_{%alpha m} cdot i_{%alpha p}(t) + %lambda, # %PSI_{%beta c}(t) = L_{%beta c} cdot i_{%beta c}(t) + L_{%beta m} cdot i_{%beta p}(t) , # %PSI_{%alpha p}(t) = L_{%alpha p} cdot i_{%alpha p}(t) + L_{%alpha m} cdot i_{%alpha c}(t), # %PSI_{%beta p}(t) = L_{%beta p} cdot i_{%beta p}(t) + L_{%beta m} cdot i_{%beta c}(t), } right none 3) / on excluding currents from equation (3) we have / left lbrace stack { i_{%alpha c}(t) ~=~ {L_{%alpha p} cdot %PSI_{%alpha c}(t) ~-~ L_{%alpha m} cdot %PSI_{%alpha p}(t) - L_{%alpha p} cdot %lambda} over {D_{%alpha}}, # i_{%beta c}(t) ~=~ {L_{%beta p} cdot %PSI_{%beta c}(t) ~-~ L_{%beta m} cdot %PSI_{%beta p}(t)} over {D_{%beta}}, # i_{%alpha p}(t) ~=~ {L_{%alpha c} cdot %PSI_{%alpha p}(t) ~-~ L_{%alpha m} cdot %PSI_{%alpha c}(t) + L_{%alpha m} cdot %lambda} over {D_{%alpha}}, # i_{%beta p}(t) ~=~ {L_{%beta c} cdot %PSI_{%beta p}(t) ~-~ L_{%beta m} cdot %PSI_{%beta c}(t)} over {D_{%beta}}, } right none (4) / where / D_{%alpha} ~=~ L_{%alpha c} cdot L_{%alpha p} - L_{%alpha m}^2 ,~ D_{%beta } ~=~ L_{%beta c} cdot L_{%beta p} - L_{%beta m}^2 . / As a result we can write the dynamic equations for electromagnet processes in problem space in the Cauchy form: / left lbrace stack { {d %PSI_{%alpha c} (t)} over {dt} ~=~ U_{%alpha c}(t) ~-~ {R_c cdot (L_{%alpha p} cdot %PSI_{%alpha c} (t) - L_{%alpha m} cdot %PSI_{%alpha p} (t) - L_{%alpha p} cdot %lambda ) } over {D_{%alpha}} ~+~ { p_п} cdot %OMEGA(t) cdot {%PSI_{%beta c} (t)} , # {d %PSI_{%beta c} (t)} over {dt} ~=~ U_{%beta c}(t) ~-~ {R_c cdot (L_{%beta p} cdot %PSI_{%beta c} (t) - L_{%beta m} cdot %PSI_{%beta p} (t) ) } over {D_{%beta}} ~-~ { p_п} cdot %OMEGA(t) cdot {%PSI_{%alpha c} (t)} , # {d %PSI_{%alpha p} (t)} over {dt} ~=~ ~-~ {R_{%alpha p} cdot (L_{%alpha c} cdot %PSI_{%alpha p} (t) - L_{%alpha m} cdot %PSI_{%alpha c} (t) + L_{%alpha m} cdot %lambda ) } over {D_{%alpha}}, # {d %PSI_{%beta p} (t)} over {dt} ~=~ {- R_{%beta p} cdot (L_{%beta c} cdot %PSI_{%beta p} (t) - L_{%beta m} cdot %PSI_{%beta c} (t) ) } over { D_{%beta} }. } right none (5) / If inductances are expressed via main and leakage ones: / alignl left lbrace stack { L_{%alpha c} = L_{%alpha m} + L_{%alpha c %sigma}, # L_{%beta c} = L_{%beta m} + L_{%beta c %sigma}, # L_{%alpha p} = L_{%alpha m} + L_{%alpha p %sigma}, # L_{%beta p} = L_{%beta m} + L_{%beta p %sigma}, } right none / then we have / D_{%alpha} ~=~ L_{%alpha c %sigma} cdot L_{%alpha p %sigma} + L_{%alpha m} cdot L_{%alpha c %sigma} + L_{%alpha m} cdot L_{%alpha p %sigma} , newline D_{%beta} ~=~ L_{%beta c %sigma} cdot L_{%beta p %sigma} + L_{%beta m} cdot L_{%beta c %sigma} + L_{%beta m} cdot L_{%beta p %sigma} , (6) / left lbrace stack { {d %PSI_{%alpha c} (t)} over {dt} ~=~ U_{%alpha c}(t) ~-~ R_c cdot {{ (L_{%alpha m} + L_{%alpha p %sigma} ) cdot %PSI_{%alpha c} (t) - L_{%alpha m} cdot %PSI_{%alpha p} (t) - (L_{%alpha m} + L_{%alpha p %sigma}) cdot %lambda } over {D_{%alpha}}} ~+~ { p_п} cdot %OMEGA(t) cdot {%PSI_{%beta c} (t)} , # {d %PSI_{%beta c} (t)} over {dt} ~=~ U_{%beta c}(t) ~-~ R_c cdot {{ (L_{%beta m} + L_{%beta p %sigma}) cdot %PSI_{%beta c} (t) - L_{%beta m} cdot %PSI_{%beta p} (t) } over {D_{%beta}}} ~-~ { p_п} cdot %OMEGA(t) cdot {%PSI_{%alpha c} (t)} , # {d %PSI_{%alpha p} (t)} over {dt} ~=~ - R_{%alpha p} cdot {{ (L_{%alpha m} + L_{%alpha c %sigma}) cdot %PSI_{%alpha p} (t) - L_{%alpha m} cdot %PSI_{%alpha c} (t) + L_{%alpha m} cdot %lambda } over {D_{%alpha}}}, # {d %PSI_{%beta p} (t)} over {dt} ~=~ - R_{%beta p} cdot {{ (L_{%beta m} + L_{%beta c %sigma}) cdot %PSI_{%beta p} (t) - L_{%beta m} cdot %PSI_{%beta c} (t) } over { D_{%beta} }},# i_{%alpha c} ~=~ { (L_{%alpha m} + L_{%alpha p %sigma} ) cdot %PSI_{%alpha c} (t) - L_{%alpha m} cdot %PSI_{%alpha p} (t) - (L_{%alpha m} + L_{%alpha p %sigma}) cdot %lambda } over {D_{%alpha}} ,# i_{%beta c} ~=~ { (L_{%beta m} + L_{%beta p %sigma}) cdot %PSI_{%beta c} (t) - L_{%beta m} cdot %PSI_{%beta p} (t) } over {D_{%beta}},# T_e(t) = 0.5 cdot p_п cdot p_f cdot left ( %PSI_{%alpha c}(t) cdot i_{%beta c}(t) - %PSI_{%beta c}(t) cdot i_{%alpha c}(t) right ), # {d %OMEGA(t)} over {dt} = 1 over J cdot left ( T_е(t) - M_в(t) right ), # {d %theta(t)} over {dt} = %OMEGA(t), } right none (7) / In accordance with equations (7) flux-linkages %PSI_{%alpha c}(t),~ %PSI_{%beta c}(t),~ %PSI_{%alpha p}(t),~ %PSI_{%beta p}(t) , angular rotor speed %OMEGA(t) and rotor rotation angle %theta(t) are variables of SMW state. Stator winding voltages and exciting moment are input parameters. / Input signals: / 1) Stator winding voltage U_{a c} (t) in a fixed system of coordinates, V. / 2) Stator winding voltage U_{b c}(t) in a fixed system of coordinates, V. / 3)Exciting moment M_ex(t) , N·m. / Output signals: / 1) Rotor angle q(t) , rad. / 2) Rotation angular speed q'(t) , rad/s. / 3) Electromechanical moment on the rotor shaft T_e(t) , N·m. / The following two signals can be additionally applied to the third output: / a) Stator winding current i_{%alpha c}(t) , А. / b) Stator winding current i_{%beta c}(t) , А. / Properties: / Stator α-winding resistance R_{%alpha c} , Ohm; / Stator β-winding resistance R_{%beta c} , Ohm; / Stator α-winding inductance L_{%beta c} , H; / Stator β-winding inductance L_{%beta c} , H; / Magnet flux from permanent magnet via stator windings I, Wb; / Moment of inertia reduced to the rotor shaft J , kg·m2; / Rotor α-winding resistance R_{%alpha p} , Ohm; / Rotor β-winding resistance R_{%beta p} , Ohm; / Rotor α-winding inductance L_{%alpha p} , H; / Rotor β-winding inductance L_{%beta p} , H; / Mutual inductance of windings along axis α L_{%alpha m} , H; / Mutual inductance of windings along axis β L_{%beta m} , H; / Number of poles p_п , pcs. / Number of power voltage phases p_f , pcs. / Initial angle of rotor rotation q(0) , rad. / Initial rotor speed q'(0) , rad/s / Initial flux-linkage %PSI_{%alpha c}(t) , V·s. / Initial flux-linkage %PSI_{%beta c}(t) , V·s. / Initial flux-linkage %PSI_{%alpha p}(t) , V·s. / Initial flux-linkage %PSI_{%beta p}(t) , V·s. / Additional output.