	2-phase to 3-phase convertor
in palette

in diagram
The unit implements the conversion of two-phase voltage to three-phase voltage. Voltage values at the output are calculated as follows: / left lbrace stack{ alignl U_a(t) ~=~ U_d(t) , # U_b(t) ~=~ - {{U_d(t)} over {2}} ~+~ {{sqrt{3} over 2} cdot U_q(t)}, # U_c(t) ~=~ - {{U_d(t)} over {2}} ~-~ {{sqrt{3} over 2} cdot U_q(t)}, } right none (1) / where U_d(t), U_q(t) are phase voltages of 2-phase current; / U_a(t), U_b(t), U_c(t) are phase voltages of 3-phase current. / The unit has 2 input and 3 output ports. / Input signals: / 1) Voltage U_d(t) , V. / 2) Voltage U_q(t) , V. / Output signals: / 1) Voltage U_a(t) , V. / 2) Voltage U_b(t) , V. / 3) Voltage U_c(t) , V. / Note: in place of phase voltages a phase currents can be applied to inputs to convert two-phase current to three-phase one.