	2-phase voltage generator
in palette

in diagram
The unit implements the model of two sine signals phase-shifted by 90 degrees: / left lbrace stack{ alignl U_d(t) ~=~ U_max(t) cdot sin(2 p cdot f cdot t), # U_q(t) ~=~ U_max(t) cdot sin(2 p cdot f cdot t + {%pi over 2}), } right none / where U_max(t) is for sine signal amplitude, / U_d(t), U_q(t) are for phase voltages of 2-phase current (output signals), / f is for frequency of signals. / The unit has 2 input and 2 output ports. / Input signals: / 1) Frequency f , Hz. / 2) Voltage U_max(t) — amplitude of signals, V. / Output signals: / 1) Voltage U_d(t) , V. / 2) Voltage U_q(t) , V.