	3-phase voltage generator
in palette

in diagram
The unit implements the model of three sine signals phase-shifted by 120 degrees: / alignl left lbrace stack{ U_a(t) ~=~ U_max(t) cdot sin(2 p cdot f cdot t), # U_b(t) ~=~ U_max(t) cdot sin(2 p cdot f cdot t + {{2} over 3} cdot %pi), # U_c(t) ~=~ U_max(t) cdot sin(2 p cdot f cdot t - {{2} over 3} cdot %pi), } right none / where U_max(t) is for sine signal amplitude, / U_a(t), U_b(t), U_c(t) are for phase voltages of 3-phase current (output signals), / f is for frequency of signals. / The unit has 2 input and 3 output ports. / Input signals: / 1) Frequency f , Hz. / 2) Voltage U_max(t) — amplitude of signals, V. / Output signals: / 1) Voltage U_a(t) , V. / 2) Voltage U_b(t) , V. / 3) Voltage U_c(t) , V.