	Simplified reducer
in palette

in diagram
The unit implements the mathematical representation of reducer without consideration of response rate of intermediate stages of mechanical transmission and phenomenon of friction in elastic elements. / Dynamic equations of the unit (two differential equations and one algebraic one): / left lbrace stack { {dq_{l}(t)} over {dt} = %omega_l(t), # {d %omega_{l}(t)} over {dt} = {M(t)} over J, # M(t) = f_dz left [ {q_eng(t)} over i - q_l(t) - k cdot %omega_l(t) right ] ; } right none (1) / where: / i is for reduction ratio; / J is for load inertia, kg·m2; / k is for friction coefficient reduced to the load shaft, N·m·s; / q_l(t) is for rotation angle of load shaft (output shaft), rad; / %omega_l(t) is for angular speed of load shaft, rad/s; / q_eng(t) is for rotation angle of engine shaft (input shaft), rad; / M(t) is for moment developed in an elastic element reduced to load shaft, N·m; / f_dz[...] is for indication of non-linearity of “dead zone” type with parameters “a” and “c”: / f_dz[x] = left lbrace stack { c cdot (x+a), ~if~ x(t) ~<~ -a, # 0, ~if~ -a ~<=~ x(t) ~<=~ a, # c cdot (x-a), ~if~ x(t) ~>~ a, } right none (2) / where a is for a half of play value, rad; / с is for coefficient of rigidity of elastic element, N·m/rad. / The unit has 1 input and 3 output signals. / Input signal: / q_eng(t) input shaft (engine shaft) rotation angle, rad. / Output signals: / q_l(t) load shaft (output shaft) rotation angle, rad. / %omega_l(t) – load shaft angular speed, rad/s. / M(t) – moment developed in an elastic element reduced to load shaft, N·m. / Properties: / Reducer transmission coefficient i; / Load inertia J, kg·m2; / Half of play value reduced to load shaft a, rad; / Coefficient of rigidity с, N·m/rad; / Friction coefficient reduced to load, N·m·s; / Load shaft (output shaft) initial rotation angle q_l(0) , rad; / Load shaft initial angular speed %omega_l(0) , rad/s;