	From the Memory
In palette

In diagram
The unit is intended to link one part of the diagram to another one located in a random place of the project. To select a source assigned by means of unit To the Memory one should double-click the unit and select a required link point from the list. / Double-click the unit to indicate the point name. A number of link points in the unit can be indicated. / The unit is vectorized and performs the procedure of extraction of global (named) variables from the dynamic memory for implementation the 2nd stage of “wireless” data transfer. / The unit is provided only with output port (-s). / The unit has a special dialog window entitled From the Memory containing 2 mini window: / · Source (for displaying the names of global variables); / · Receiver (for displaying the list of names of global variables in that, which remain in the project by the moment of dialog window opening). / Dialog window Filter is intended to sort out variables as per their name type. / When the dialog window is opened for the first time the mini window Source will contain the names of all global variables generated by the moment by units To the Memory, while the mini window Receiver is empty (see the left screen button of the dialog window below). / If any global variable needs to be extracted from the memory as an output signal, e.g., Nтепл, then: / · highlight the variable in the mini window Source by the mouse cursor; / · single-click the right single-arrow button with the mouse left key: name of the variable will be shifted from the left mini window (Source) to the right-bottom mini window (Receiver); / · close the dialog window by clicking the Ok button: the diagram window will be then re-drawn and the considered unit From the Memory will have one (scalar) output port. / Should two or more global variables be extracted from the dynamic memory the above described sequence of operations is to be repeated for other variables. / Right double-arrow button is intended to shift all names from the left mini window to the right mini window. / Left single-arrow button is intended to shift the name of one variable from the right mini window to the left mini window. / Left double-arrow button is intended to shift all names from the right mini window to the left mini window. / Two buttons (with by-pass arrows and a list) are intended to shift (manually sort out) names of variables up/down in the mini window Receiver. / Properties: Any properties shall not be set for the operation of the unit. / Notes: / 1. If a number of global (scalar or vector) variables to be extracted from the dynamic memory is two or more then, when closing the dialog window, the Diagram Window will be re-drawn and the considered unit From the Memory will have got a number of output (scalar or vector) ports equal to a number of global variables to be extracted. / 2. If a number of variables is considerably big and their full list cannot be housed in one of mini windows then for displaying the whole content a standard scrolling mechanism is provided for such window.