	Phase Portrait
In palette

In diagram
The unit is vectorized and has two inputs, implements the display of current simulation results on the phase plane for one pair or simultaneously for a number of pairs of phase variables. / The unit has two vectorized inputs: the abscissa value is taken from the first input the ordinate value is taken from the second input. Dimensions of input signals shall be the same. / The unit applies the graphic window similar to the one applied by the unit Time diagram. / Dimensions of inputs shall be the same. / Properties: Any properties shall not be set for the operation of the unit.