	Diagram X on Y
In palette

In diagram
The unit is vectorized and implements the output of dependance of vector Y (second input) on vector X (first input). / The unit is intended to display current simulation results in the form of diagram Y(t,x) plotting the curve y(t) = f(x,t) after each step of integration (calculation), where x is for the vector containing time-independent constant components. / This unit can be used for displaying calculation results in linear-distributed dynamic problems where, for example, vector x is the vector of relative space coordinates in the item being simulated, while vector-function y(t) describes non-stationary distribution of a physical value in the item under simulation. / Properties: / · Number of diagrams – natural number N. If number 3, for example, is entered the unit will have 6 input ports: ports at the left for entering data corresponding to abscissa coordinates and ports at the bottom for entering vector-function y(t) values. / The unit applies the graphic window similar to the one applied by the unit Time diagram. / Dimensions of inputs shall be the same.