	Non-linear equation F(y) = 0
in palette	| vectorized |

in diagram
The unit is intended to calculate values in algebraic loops and implements the iterative solution for system of non-linear algebraic equations (NLAE) by a method preset in the task settings. The program core executes automatic selection of unit output values for the maximum approximated fulfillment of condition: unit output vector values are equal to 0: / vec{u}(t) simeq vec{0} ~dlrarrow~ u_i(t) simeq 0, ~ i=1... n . / Property: / Initial approximation – number or vector setting the initial approximation for unit output signal. / Samples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Initial approximation [1] / Named definition of properties: / Name Value / Initial approximation [y0] / Vector definition of properties: / Name Value / Initial approximation [0, 1] / Notes: / On default the unit processes a scalar input signal. / Named property are set up as local variable of model (or submodel) in Parameters tab or as global signal of the project via Graphics → Signals main menu option.