	Output contact
In palette

In diagram
Records the executive system variable from the unit input. / Properties: / Contact name – name of the variable the unit records a signal in. / Variable name format – a rule for generation of the name of the variable to be read out. / Declare in base – a flag indicating whether there is a need for creation of the variable in the base of system signals. / Base request for a name – request from the data base in order to generate a name of the variable to be read out. / Functional plan – name of diagram file, which is to be transferred to on double-clicking the object. / Component to be debugged – name of a component to be installed when transferring to another diagram in debugging mode. / Translate to s3 — a flag indicating whether there is a need for delivering the variable from the diagram to the executive system in remote debugging mode.