	Vector amplifier
In palette

In diagram
The unit is vectorized and implements amplification function for input signal momentary value (multiplication of input value elements by vector elements of a preset amplification coefficient): / y_i(t) = k_i cdot u_{i}(t) , / where u_{i}(t) is for the i-th element of input vector signal, k_{i} is for the i-th vector element of amplification coefficients; vec{k} , y_i(t) is for output vector signal element vec{y}(t) . / Output dimension is the same as dimension of input and amplification coefficient vector. / Properties: / Amplification coefficient vector – amplification coefficient vector vec{k} .