	Selection against an active element
In palette

In diagram
The unit is vectorized and executes procedure for selection an element from the vector against a control vector active element as per the following algorithm: / left ldline stack { CYCLE ~ i = 1 ... N # IF ~u_{1,i}(t) > 0 ~ THEN ~ y(t) = u_{2,i}(t); ~ CYCLE TERMINATION # END OF CYCLE} right rdline , / where vec{u_1}(t) is for control vector; vec{u_2}(t) is for vector of values being selected; N is for dimension of inputs. / Properties: any properties are not required for the operation of the unit.