	Limiter
In palette

In diagram
The unit is vectorized and implements limitation of input value: / y_i(t) = left lbrace stack{ alignl u_i^min, ~ if ~ u_i(t) < u_i^min # alignl u_i(t), ~ if ~ u_i^min < u_i(t) < u_i^max # alignl u_i^max, ~ if ~ u_i(t) > u_i^max} right none , / where u_i(t) is for vector element of input signals; y_i(t) is for vector element of output signals; u_i^min,u_i^max are for i-th vector elements of minimum and maximum unit values. / Properties: / Input minimum value — vector of values u^min limiting the input signal “at the bottom”. / Input maximum value — vector of values u^max limiting the input signal “at the top”. / Note: by default the unit implements limitation for scalar input signal.