	Signal reading
In palette

In diagram
The unit reads out data from a local list of project signals (or from the list of signals connected to the data base). On double-clicking the unit, the editor for the list of read out variables appears: / Variable name is set in the field “Signal Name”. A devoted signal corresponds to each output of the unit. / Purpose of the table fields: / No. — serial number of the signal (and of the unit output, correspondingly) is assigned. / ID – identifier of the signal (output). / Source – description of signal “departure point” (wherefrom the signal comes). / Marking – signal (or signal source) marking. / Signal (setting) – signal designation or name. It is used when creating algorithms for generation of signals (settings) from control units for gates, motors, etc. / Signal name – name of a variable to be read out from the data base. / Unit name is assigned in the bottom portion. To the right there are options, which can be used for setting the unit appearance in the diagram, its heading display and layout of unit ports. / Properties: / Auto reset. / Calculate with a one-step delay.