	NOT XOR
In palette

In diagram
The unit performs the elementwise NOT XOR (exclusive-NOR) operation for input signals. On default, the unit implements the operation for two input signals: / y(t) = left lbrace stack{ alignl 1, ~ if ~ u_1(t) = 1, ~"and" ~u_2(t) = 1;# alignl 0, ~ if ~ u_1(t) = 1, ~"and" ~u_2(t) = 0;# alignl 0, ~ if ~ u_1(t) = 0, ~"and" ~u_2(t) = 1;# alignl 1, ~ if ~ u_1(t) = 0, ~"and" ~u_2(t) = 0; } right none , / where y(t) is for the output signal of the unit (scalar) , u_1(t),~u_2(t) are for the input signals (scalars). / The operation algorithm for the number of input signals, more than two: / y(t) = left lbrace stack{ alignl 0, ~ if only one of ~u_i(t) = 1, ~" all the others"~u_i(t) = 0;# alignl 1, ~ for other cases. } right none / Properties: / Number of ports — indicates the number of input signals of the unit.