	T trigger
In palette

In diagram
The unit is vectorized, it implements a toggle trigger that changes its state under change of a logical input signal from 0 to 1 (for the "by leading edge" type of complementing input), or vice versa, under change of the input value from 1 to 0 for the "by trailing edge" type of complementing input. / The unit algorithm for the "by leading edge" type of input: / y(t) ~=~ neg {y(t- %DELTA t)}, ~if~ u(t)=1 = neg {u(t- %DELTA t)} . / The unit algorithm for the "by trailing edge" type of input: / y(t) ~=~ neg {y(t- %DELTA t)}, ~if~ u(t)=0 = neg {u(t- %DELTA t)} . / If the input type is set to "by leading edge and trailing edge", then for any change of the input logic signal the trigger will change its state: / y(t) ~=~ neg {y(t- %DELTA t)}, ~if~ u(t) ~=~ neg {u(t- %DELTA t)} , / where y(t) is for the output signal vector , u(t) is for the input signal vector and NOT is for the NOT logical operation designation. / Properties: / Initial conditions – the initial values of the output logic vector signal. / Add an inverted output – indicates the presence of an inverted output. / Type of complementing input (by leading edge, by trailing edge, by leading edge and trailing edge) – the condition of actuation of the complementing input.