	Switching off delay
In palette

In diagram
The unit implements a delay (waiting of confirmation) of an input signal over the course of specified time under change of the input logic signal from 1 to 0: / y(t) = left lbrace stack{ alignl 1, ~ if ~ u(t) > 0.5 ; # alignl 0, ~ if ~ u(t) < 0.5~"in the course of time"~ T_2,} right none / where y(t) is for the unit output signal , u(t) is for the input signal , T_2 is for the switching off confirmation time constant. / Important: The unit output can be set to either 0 or 1. / Properties: / Confirmation times array, sec – the switching off delay T_2 . / Confirmation time representation – if representation of the "Entry” is specified, then delay time will be taken from the second extent entry. / Comparison of the units of switching off delay, switching on delay, and together switching off and switching on delay: / When applying the square signal as an input signal (the unit signal is present during 10 sec, and there is not any signal during 20 sec), then the following pictures will be seen at the outputs of these units (with 6 sec switching off delay, 4 sec switching on delay, and together 2 sec switching on and 3 sec switching off delays, respectively): / Note: if any real (rather then logical) signal is applied to the unit input, then the unit will be considered as switched on in case of u(t) > 0.5 and switched off in the case of u(t) < 0.5 :