	Pulse by leading edge
In palette

In diagram
The unit forms the pulse of unit value with duration of one step of integration, under change of the input value from zero to one: / y(t) = left lbrace stack{ alignl 1, ~ if u(t) = 1 = neg u(t- %DELTA t) = neg 0; # alignl 0, ~ for all other cases; } right none , / where y(t) is for the unit output signal , u(t), ~ u(t- %DELTA t) are for the input signal at current time and at previous time step of integration . / Properties: any properties are not required for operation of the unit. / Note: if a real (rather then logical) signal is applied to the unit input, then the unit will be considered as one in case of u(t) > 0.5 and zero in the case of u(t) < 0.5 .