	Pulse
In palette

In diagram
The unit generates a pulse with a given duration when an input signal changes from zero to one. / The unit algorithm: if the input signal is changed from zero to one (or nonzero), then the unit will form the logical one at the output within a specified time. In this case the unit neglects variations of the input signal during the pulse time (while the output is 1). / Properties: / Pulse duration – the time the unit forms the logical one at the output. / Duration is defined by – the representation of the pulse duration: through an extent entry or through the “Pulse duration” parameter of the unit. / Comparative example of the unit operation: / Consider three units with the pulse duration of 1, 4 and 10 seconds respectively. Therewith, we shall feed the same square signal with the full period of 7 seconds to the units inputs (duration of the first half-period is 2 sec, and the second one is 5 sec). Calculation time – 30 sec: / Consider the graphs of the pulses obtained at the outputs of the units (the pink curve corresponds to the square input signal, the black curve corresponds to the pulse signal): / As can be seen from the graphs, the unit generates pulses of the strictly specified duration and only when the input signal varies from 0 to 1. In this case, the unit does not take into account changes of the input signal during generation of a pulse (see the graph for the 7 sec pulse).