	Pulse with no more than specified duration
In palette

In diagram
The unit generates a pulse of a specified duration and no more, under changes of input signal from zero to one. / The unit algorithm: if the input signal is changed from zero to one (or to nonzero), then the unit will form the logical one at the output within a specified time. Therewith, if the input signal disappears before the end of the specified pulse duration (i.e., it becomes equal to 0), then the unit will take it into account and stop to feed the pulse to the output. / Properties: / Pulse duration – the time the unit forms the logical one at the output. The pulse duration can be less than the specified duration, if the input signal is lost. / Duration is defined by – the representation of the pulse duration: through an extent entry or through the “Pulse duration” parameter of the unit. / Comparative example of the unit operation: / Consider three units with pulse duration of no more than 1, 4 and 10 seconds respectively. Therewith, we shall feed the same square signal with the full period of 7 seconds to the units inputs (duration of the first half-period is 2 sec, and the second one is 5 sec). Calculation time – 30 sec: / Consider the graphs of the pulses obtained at the outputs of the units (pink curve corresponds to the square input signal, and black curve corresponds to the pulse signal): / As can be seen from the graphs, the unit generates pulses with no more than the specified durations and only until the input signal varies from 0 to 1 and remains equal to 1. The last two graphs are the same, although the specified pulse durations are different for these units.