	Pulse with prolongation
In palette

In diagram
The unit generates a pulse of duration not less than a specified duration, under changes of input signal from zero to one. Therewith, the pulse is prolonged again for the specified duration if the next changing of the input from 0 to 1 takes place during the process of generation of the previous pulse. / The unit algorithm: if the input signal is changed from zero to one (or to nonzero), then the unit will form the logical one at the output within a specified time. Therewith, during the entire duration of the pulse (while 1 is at the output of the unit) the unit also takes into account changes of the input signal, and in the next changing from 0 to 1 the pulse is formed (“picked up”) again and the pulse duration is considered to start from the moment of the last change of the input from 0 to 1. / Properties: / Pulse duration – the time the unit forms the logical one at the output. / Duration is defined by – the representation of the pulse duration: through an extent entry or through the “Pulse duration” parameter of the unit. / Comparative example of the unit operation: / Consider three units with pulse duration of 1, 4 and 10 seconds respectively, with prolongation. Therewith, we shall feed the same square signal with the full period of 7 seconds to the units inputs (duration of the first half-period is 2 sec, and the second one is 5 sec). Calculation time – 30 sec: / Consider the graphs of the pulses obtained at the outputs of the units (pink curve corresponds to the square input signal, and black curve corresponds to the pulse signal): / As can be seen from the graphs, the unit generates pulses with duration which is not less than the specified duration. In this case, during generation of a pulse the unit takes into account new changes of the input signal from 0 to 1 (see the graph for the 7 sec pulse).