	Normally closed contact of the relay
In palette

In diagram
The unit realizes the logical AND-NOT operation for the unit input and a value applied to the corresponding control winding of the relay: / y(t) = left lbrace stack{ alignl neg x_relais(t), ~ "if" u(t)=1; # alignl 0, ~ "if" u(t)=0; } right none / where y(t) is for the output signal of the unit, x_relais(t) is for the value (state) of the relay, neg x_relais(t) is for the logical negation of the relay state and u(t) is for the input signal of the unit. / In other words, if the logical one is applied to the input of the unit, then the value opposite to the relay control winding will be formed at the output, i.e. the relay will be cut off. If the logical zero is applied to the input of the unit, then the logical zero will always be formed at the output without regard to the relay state. / To see the algorithm structure, press the right button on the unit and select the item "Actions" → "Enter the submodel". Signal transmission from the control winding of the relay is realized by the unit named From memory. / Properties: / Relay name – the name whereby a control action is defined.