	Normally opened contact of the relay with delay for opening
In palette

In diagram
The unit realizes the logical AND operation with delay for opening for the unit input and a value applied to the corresponding control winding of the relay: / y(t) = left lbrace stack{ alignl 1, ~ if u(t)=1; # alignl 1, ~ if u(t)=1;~"and"~ x_relais(t)=1 ~for the last T_2 seconds; # alignl 0, ~ if u(t)=0; } right none / where y(t) is for the output signal of the unit, x_relais(t) is for the value (state) of the relay, and u(t) is for the input signal of the unit. Delay for opening applies only to relay switching-off. / To see the algorithm structure, press the right button on the unit and select the item "Actions" → "Enter the submodel". Signal transmission from the control winding of the relay is realized by the unit named as From memory. Delay for opening is realized by the unit named as Delay for switching off. / Properties: / Relay name – the name whereby a control action is defined. / Delay time – the delay time T_2 when relay contact is turned off.