	Sensor
In palette

In diagram
The unit is similar to the “Input contact” unit, with addition of displaying of the measured value. / The unit realizes reading of a variable, its transmission to the unit output and also displaying of the variable value on the circuit window in a user-defined format. / In the local debugging mode it is equivalent to a constant. For remote debugging, the unit reads a variable from the executive system. Properties: / Default value – the value at the output of the unit, it can be a vector value. / Contact type – the data type of the output variable when generating a code for full-scale model. / Contact name – the name of the variable that is read by the unit. / Variable name format – the name generation rule of the variable to be read. / Add to the signal database – the flag that indicates whether to form this variable in the system signal database. / Name request from the database – the request from the database to form the name of the variable to be read. / Operational plan – the name of the chart file you need to go when double-clicking on an object. / Debugged component – the name of the component which will be installed when changing over to another chart in debugging condition. / Properties effecting on appearance of the unit only: / Sensor type – the character or line that explains type of the value measured by the sensor and used in left side of the sensor picture. / Total number of characters – the number that indicates the total number of digits (before and after the decimal point) when displaying the sensor readings. / Number of decimal places – the number that indicates the number of digits after decimal point when displaying the sensor readings. / Number format – the flag that indicates in what format it is necessary to output the value of the measurand. / Sensor description – the text in a custom format (arbitrary) that describes the sensor, the measurand, etc. It is displayed on default in the unit caption.