	Record by condition
в палитре

на схеме
The unit is a simplification (a special case) of the «Key-3» type unit. If the condition is fulfilled (if logical signal is at the IF input), then input values will be transferred to the output, otherwise at the output. / The unit is a submodel (assembly), which includes the "Key-3" type unit. For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / The unit is vectorized and realizes the slave key function according to the algorithm: / {y(t) = 0},~if~{a(t)<0,5} newline {y(t) = x(t)},~if~{a(t) geslant 0,5} , / where { a(t) } is for the vector of control signals at the first input of the unit; { x(t) } is for the vector of input signals at the second input of the unit; { y(t) } is for the vector of signals at the output. / Property: / List of signals – the list of variables used as components of the { a(t) } vector. The list consists of some names of variables that are recorded line by line (one line – one variable).