	Signal is greater than setting
In palette

In diagram
The unit is a relay element with a dead zone: if an input signal is greater than the setting value, then the unit will generate the logical one at the output; if the input signal becomes lower than the setting value (with provision for the return zone, if specified as non-zero) then the unit will generate the logical zero at the output: / y(t) = left lbrace stack{ alignl 1, ~ "if" ~ u(t) ~>~ u_0 # alignl 0, ~ "if" ~ u(t) ~<~ u_0 - a} right none , / where u(t) is for the input signal; y(t) is for the output signal; a,~u_0 are for the values of the return zone and the setting respectively. / The unit is a submodel. For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / Properties: / Setting — the setting value, with which the input signal is compared. In other words, this is the high bound of the relay element switching-over. / Return zone — the value which is subtracted from the setting to form the low bound of the relay element switching-over.