	Threshold (operating level)
In palette

In diagram
The unit is a relay element with a dead band ; it forms the logical one or the logical zero at the output in accordance with the following algorithm: / Two signals are applied to the unit input and these signals are compared. If their difference exceeds the operating level, then the unit will form the logical one at the output. If the difference between two input signals become less than the operating level (with provision for the return band ), then the unit will form the logical zero at the output: / y(t) = left lbrace stack{ alignl 1, ~ "if" ~ [u_1(t)-u_2(t)] ~>~ %epsilon_0 # alignl 0, ~ "if" ~ [u_1(t)-u_2(t)] ~<~ %epsilon_0 - a} right none , / where u_1(t),~u_2(t) are for the unit input signals; y(t) is for the output signal; a,~%epsilon_0 are for the values of the return band and operating level respectively. / The unit is a submodel. For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / Properties: / Operating level — the setting with which the difference of input signals is compared. / Return band — the value which is subtracted from the setting to form the low bound of switching-over.