	Double threshold
In palette

In diagram
The unit is a relay element with a dead band and two outputs; it forms the logical one or the logical zero at its outputs in accordance with the following algorithm: / Two signals are applied to the unit input and these signals are compared between themselves. If their difference exceeds the high limit, then the unit will form the logical one at the first output. If the difference between the first input and the second input becomes less than the low limit, then the unit will form the logical one at the second output. Otherwise (if the difference is between the high and low limits, with provision for the return band value), the logical zero is formed at the outputs: / y_1(t) = left lbrace stack{ alignl 1, ~ "if" ~ [u_1(t)-u_2(t)] ~>~ %epsilon_1 # alignl 0, ~ "if" ~ [u_1(t)-u_2(t)] ~<~ %epsilon_1 - a} right none newline y_2(t) = left lbrace stack{ alignl 0, ~ "if" ~ [u_1(t)-u_2(t)] ~>~ %epsilon_2 + a# alignl 1, ~ "if" ~ [u_1(t)-u_2(t)] ~<~ %epsilon_2} right none , / where u_1(t),~u_2(t) are for the unit input signals; y_1(t),~y_2(t) are for output signals; a,~%epsilon_1,~%epsilon_2 are for the return band value and difference variation limits (trip limits). / The unit is a submodel. For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / Properties: / High limit – the upper setting with which difference of input signals is compared. / Low limit – the lower setting with which difference of input signals is compared. / Return band – the value which is subtracted from the upper setting and added to the lower setting to form dead bands. Dead band width of the unit is the same (both above and below).