	Dead zone (variable)
в палитре

на схеме
The unit implements a linear element algorithm with a gain equal to 1 and a dead zone, which varies depending on an input signal at the second input port. / The unit is a submodel. For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / Input signals: / Input – the input signal of the unit. / Dead zone – the value of the "dead zone". If the input signal is less than the absolute value of the dead zone, then the unit output will be equal to 0. / Output signal: / Output – it is equal to 0, if the input signal in absolute value is less than the dead zone. Otherwise, the output is equal to the difference of the input signal and the dead zone value, multiplied by the sign of the input signal. / Properties: any properties are not required for operation of the unit.