	Sorting pointer
In palette

In diagram
The unit is used for forced sorting of other units in required sequence by the user. / When initializing a model in the “SimInTech” Software system, sorting of all units of an analytical model for further integration of the model takes place: at every step of the integration the units are calculated one after another in the presorted order. Sometimes it is necessary that execution (calculation) of one unit would be executed strictly after another unit. The unit connected to the output of the sorting pointer is executed strictly after units connected to the inputs of the sorting pointer. In other words, the unit is an instruction for the “SimInTech” Software system to sort the next unit (connected to the output) strictly after the preceding units (connected to the inputs). / The output signal of the sorting pointer unit is always equal to an input signal at the first input. / Properties: / Port capacity — the number that indicates the amount of the additional input signals of the unit.