	Elementwise M from N
In palette

In diagram
The unit is an analogue to the M from N logical unit, it is vectorized and implements the majorization operation to the following algorithm: / Notations of the input and output signals: / y(t)~"and"~y_i(t) — are for the output vector and the i-th element of the output vector. / u_1(t),~u_2(t)~...~u_N(t) — are for the input vectors. / M — is for the parameter for comparison with the total number of inputs N . / u_{1,i} — is for the i-th element of the 1-st input vector (etc.) / Dimensions of the input and output vectors shall coincide. / Dim — the number of signals in the input vectors (and in the output vector). / The unit algorithm: / alignl for~(i = 1, Dim)~do~begin newline alignl~C = 0 newline alignl~if~(u_{1,i} > 0)~then~C = C + 1; newline alignl~if~(u_{2,i} > 0)~then~C = C + 1; newline alignl~... newline alignl~if~(u_{N,i} > 0)~then~C = C + 1; newline alignl~if~(C >= M)~then~y_i(t) = 1~else~y_i(t) = 0; newline alignl end; / Thus, at the output for each of i (for each of the signals of the input vectors) the logical one will be formed, if C >= M takes place (number of non-zero i-th signals in the input vectors exceeds the parameter M ). If C < M takes place, then the logical 0 will be formed at the output (for each of the i-th element). / Properties: / Port capacity — the natural number N . / Number of the input True for actuation — the natural number M .