	Relay external contact
в палитре

на схеме
The unit is a submodel. For checking the algorithm structure one shall press “Actions” → “Enter the submodel” with the right button. / The unit implements the logical AND operation for the unit input and the value indicated in the unit parameters (an analogue to the relay control winding for the Relay normally opened contact unit). Thus, the contact name is specified directly within the submodel. / Properties: / Variable name — the name of the variable for which (and for the unit input) the AND operation is implemented. / Initial status (0 or 1) — the initial condition of the unit output.