	Number of linear equation
in palette	| vectorized |

in diagram
The unit is used along with units “Coefficients of linear equation” and “System of linear equations results”. / The unit is a counter for the number of equations in a system with a preset name. / This unit returns a vector of unique numbers of system of linear equations lines (equations) at the output. When initializing the diagram, a system of linear equations solver-object is initialized, which is common for the diagram and has unique name <solvername> and contains the counter of number of equations. At the same time the considered system can be combined with basic Jacobian used for implicit methods of integration, moreover, independent system of linear equations can also exist. This unit, on initialization of the diagram, adds the number of equations <equcount> set up in the unit properties to this counter and generates the vector of the numbers of equations with dimension <equcount> at the output. During calculation this unit outputs do not change. / Properties: / Name of system of linear equations solver – name of solver (line <solvername>), which processes (solves) system of linear equations . Must be the same for all units “Number of linear equation”, “Coefficients of linear equation” and “ system of linear equations results” belonging to the same system. / Number of equations – natural number <equcount> designating the number of equations added by this unit to the system <solvername>.