	Coefficients of linear equation
in palette	| vectorized |

in diagram
The unit is used along with units “Number of linear equation” and “system of linear equations results”. / The unit sets up coefficients (matrix A of the system) and values of right parts (vector B) for equations (numbers of equations) indicated at the first input. / Vector of numbers of lines (numbers of equations) of a system of linear equations with name <solvername>, which are formed by means of unit “Number of linear equation”, is set up for the first input of this unit. / Vector of numbers of columns, which is generated as per the following rule, is delivered to the second input of this unit: / [<№ of column 1 of line 1> . . . <№ of column 1 of line N>, / <№ of column 2 of line 1> . . . <№ of column 2 of line N>, / <№ of column M of line 1> . . . <№ of column M of line N>] / where: / N is for number of equations determined via the dimension of the vector of numbers of lines at the unit first input; M is for number of filled columns for each line that is set up by the vector of numbers of lines at the unit first input. / Vector of SLAE coefficients, which are set up as per the following rule, is delivered to the unit third input: / [<Coeff. of column 1 of line 1> . . . <Coeff. of column 1 of line N>, / <Coeff. of column 2 of line 1> . . . <Coeff. of column 2 of line N>, / <Coeff. of column M of line 1> . . . <Coeff. of column M of line N>] / Vector of system of linear equations right parts for lines, which are set up by the vector of numbers of lines at the unit first input, are set up at the unit fourth input. / The unit for setting up coefficients in principle allows numbers of sparse matrix filled columns to be switched over in the process of calculation, which enables the implementation of reconfigurable networks. In case numbers of columns are the same for one number of a line, appropriate matrix coefficients are summed up; this enables a correct analysis of parallel circuits for nodal tasks. / Property: / Name of system of linear equations solver – name of solver (line), which processes (solves) system of linear equations. Must be the same for all units “Number of linear equation”, “Coefficients of linear equation” and “ system of linear equations results” belonging to the same system.