Input circuit
Input circuit 2
Control
	Controllable current source
in palette	| System of linear equations|

in diagram
The unit represents a model of linear resistance with current source. / Internal structure of the unit is given in Figure 1: / Figure 1 – Internal structure of unit “Controllable voltage source” / This unit by means of indirect connection generating units transmits conductivity values (KJ), which are calculated as 1/Rs, and values of currents (Isrc), set up from input “Control”, to electric circuit internal nodes connected to this element. At the same time the value of own node number (NSELF) from the first input is transmitted as the value of adjacent node number (NJ) and vice versa. Source current is supplied with the positive sign to input 2 and with the negative sign to input 1. / Property: / Shunt resistance, Ohm – a number setting up the shunt resistance value. / Examples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Shunt resistance, Ohm [1e8] / Named definition of properties: / Name Value / Shunt resistance, Ohm [Rsh_1] / Notes: / Unit property can be scalar only. / Named property is set up as local variable of model (or submodel) in Parameters tab or as a global signal of the project via Graphics → Signals main menu option.