Input circuit
Input circuit 2
Control
	Controllable conductivity
in palette	| SLAE |

in diagram
The unit is similar to unit Linear electric resistance (described by Ohm's law) with an only difference – the element resistance is not a constant: / {u_1(t) - u_2(t)} over {R(t)} = I(t) , / where: / u_1(t) , u_2(t) are for potentials of nodes this element is to be connected to; / R(t) is for time-variant resistance value (conductivity supplied to the control input is a value reciprocal to the resistance); / I(t) is for current through element. / Internal structure of the unit is given in Figure 1: / Figure 1 – Internal structure of unit “Controllable conductivity” / This unit by means of indirect connection generating units transmits conductivity values (KJ), which is to be supplied to the control input, and values of currents (Isrc), equal to zero, to electric circuit internal nodes connected to this element. At the same time the value of own node number (NSELF) from the first input is transmitted as the value of adjacent node number (NJ) and vice versa. / Properties: no properties are required for operation of the unit.