Input circuit 1
Input circuit 2
output circuit 1
output circuit 2
	Ideal transformer
in palette	| System of linear equations |

in diagram
The unit represents an ideal transformer model described by the following system of equations: / left lbrace stack{ alignl {U_{i n}(t)} = k cdot U_{o u t}(t), # alignl {I_{o u t}(t)} = k cdot I_{i n}(t); } right none / where: / k is for transformation coefficient; / U_{i n}(t) is for input voltage; / U_{o u t}(t) is for output voltage; / I_{i n}(t) is for current in primary winding; / I_{o u t}(t) is for current in secondary winding. / This system of equations can be represented as two interconnected nodes. The structure of ideal transformer model is given in Figure 1: / Figure 1 – Internal structure of unit “Ideal transformer” / Property: / Transformation coefficient – number k . / Shunt resistance, Ohm – a number defining shunt resistance value. / Node initial voltage, V – initial condition on voltage. / Examples for filling in the dialog window for unit properties: / Numerical definition of properties: / Name Value / Transformation coefficient 3 / Shunt resistance, Ohm [1e12] / Node initial voltage, V 0.5 / Named definition of properties: / Name Value / Transformation coefficient k_transf / Shunt resistance, Ohm Rsh_1 / Node initial voltage, V U_0 / Notes: / Unit properties can be scalar values only. / Named property is set up as local variable of model (or submodel) in Parameters tab or as a global signal of the project via Graphics → Signals main menu option.