Table editor window
Table editor window is a form containing tools for filling and editing a table. This window includes the following elements: algorithm for table calculation and description, message box, table setting panel and tool bar (see figure 1). / Figure 1 – Table editor window / Algorithm for table calculation and description / Algorithm for table calculation and description is a field similar to global parameters editor window and allows a table to be filled in automated manner using values, variables and functions described in global parameters editor window. Working tools for this element are also similar to the tools used for working with global parameters editor window, and include: Clean table, View variables, Construct relation, Stepwise debugging and Stop debugging (see item “Global parameters editor window”). / Let us consider an example of constructing an algorithm for table calculation and description as exemplified by creation of EKN 125-140 pump head capacity table. / //PUMP HEAD AND DISCHRGE PERFORMANCE / //Set up as a table function for two arguments: discharge and rotor speed / //The following algorithm is implemented in the below text. / //Chipped pump performance at the rated speed is given as a supporting curve / //H0=f(Q), where H0 is for head, m; Q is for volumetric discharge, m^3/hour / //Curves for other values of frequency are determined via the relation: / //H(Q,n)=H0(Q,n0)*[n/n0]^2 / //Chipped pump performance / H0 = [1950 / 1950 1945 1940 1936 1925 / 1900 1855 1800 1730 1640 / 1640]; / Q = [-90 / 0 10 20 30 40 / 50 60 70 80 90 / 1000]; / n0 = 49.65; //Frequency at which the performance is chipped, Hz / r0 = 956; //Water density, at which the performance is obtained / //Array of frequencies, for which the performance is calculated / Y = [0 2 4 6 8 // filling Y column / 10 15 20 25 30 / 35 40 45 n0 50 / 50.5 51 51.5 52 / 100]; / const Nx = 12; //Number of points for discharge (equal to the size of arrays H0 and X) / const Ny = 20; //Number of points for frequency (equal to the size of array Y) / var M[Ny,Nx]; //Head and discharge performance, atm / var X[Nx]; //Volumetric discharge, m^3/s / for (i = 1,Nx) X[i]=Q[i]/3600; // Filling X row / for (i = 1,Nx - 1) // Filling table boxes / for (j = 1,Ny - 1) / M[j,i] = 1e-4*r0*H0[i]*(Y[j]/n0)^2; / //The last table row is a copy of the next-to-last one / for (i = 1,Nx) / M[Ny,i] = M[Ny - 1,i]; / //The last table column is a copy of the next-to-last one / for (j = 1,Ny) / M[j,Nx] = M[j,Nx - 1]; / Row Y is filled by setting a matrix-string in an explicit form. Column X is filled in the for cycle with the contents of boxes of this column accessible through record X(i). 2-D table named M is used for the head capacity and, thus, the boxes of this table are accessible through record M(j, i), where j is for column number, i is for row number. Contents of boxes M(j, i) are calculated in the for double cycle. / To fill the table automatically by performing the written calculation algorithm, command of Clean table menu shall be used. When filling the table automatically, there will be no need for you to set manually the number of columns and rows, instead it will be enough for you to indicate a correct calculation algorithm for the box content of the boxes and to specify the type of a table, then the program will automatically set the dimensions of the table (see figure 2). / Figure 2 – Calculated table / One-dimensional table is filled in the same way. For that a record such as for ... for ... M(i,j) = f(i,j) can be used. / To plot the table curve select curve plotting type (How to plot a curve, i.e., axis of abscissas) and activate Plot table curve command, see figure 3: / Figure 3 – Curve plotted for calculated table / Message box / Message box is the same as the message box of global parameter editor (see “Global parameters editor window – Message box”). / Table setting panel / Table setting panel allows a number of columns, number of rows, type of table, table curve plotting sequence, name of matrix, name of column array and name of row array to be edited. Names of matrix, column array and row array are used for setting the table contents in algorithm of table calculation and description (see the example in item Algorithm of table calculation and description). / Tool bar / Tool bar contains commands, which allow the table contents to be controlled: the table to be transposed, columns and roes to be moved, the table to be checked, rows and columns to be sorted in ascending/descending order. / When Import table is activated, import table dialog window is displayed from clipboard (see figure 4). / Figure 4 – Import table dialog window / In the process of import of the table it is analyzed in order to detect available separators and preliminarily split it into boxes. If boxes need to be split in another manner the splitters panel shall be edited. Besides, a field to be pasted into a target table can be selected. The whole import area is selected by default. Prior to import the box contents can be manually corrected. / On activation of Import table from file, first select file dialog window and then import table will be displayed. As for the rest the import procedure is the same. / Check table command can be used when the table contents is filled manually. В этом случае, таблица будет проверена на наличие не конвертируемых в число записей в ячейках. In case inconvertible records are detected a dialog window suggesting to correct them appears (see figure 5). / Figure 5 – Dialog window of corrections of inconvertible records / Corrections of both current box contents and all similar errors of this table can be disabled. Table checking procedure is executed every time during import of the table. / In order to sort rows/columns in ascending/descending order a required column/row shall be selected (by pressing the fixed row/column box) and one of the commands: Sort ascending or Sort descending shall be activated.