Command line options
Command line start format: / mmain.exe <general program options> "project 1 file name" <project 1 start options> ... "project 2 file name" <project 2 file options> / or / mstarter.exe <general program options> "project 1 file name" <project 1 start options> ... "project 2 file name" <project 2 file options> / mmain.exe – software system main process name (graphic shell); / name of starter program mstarter.exe can stay instead of mmain.exe (it will be terminated immediately after starting and transmit a command to mmain.exe). / General program options of command line: / /exitonstop – automatic program exit on termination of counting / /exitonclose – automatic program exit on closing the last diagram window / /hidemenus – animation and diagram editor windows will be started without main menus / /nomainform – hide the main program window / /minmainform – minimize the main application window / /nohotkeys – lock up hot keys processing / Project file start options: / /nomenu – project will be started without main window menu / /nopanels – project will be started without main window menu and toolbar / /noborder – project will be started without diagram window border / /stoponclose – project will be automatically terminated on the program closing / /start – start the project (or package) on loading the file / /minimize – run the project with minimized diagram window / /run – run the project (or package) for calculation on loading the file / /left <integral number> – sets up the left coordinate of the project diagram window / /top <integral number> – sets up the top coordinate of the project diagram window / /width <integral number> – sets up the width of the project diagram window / /height <integral number> – sets up the height of the project diagram window / /x <real number> – sets up the coordinate of the diagram center in horizontal plane / /y <real number> – sets up the coordinate of the diagram center in vertical plane / /scale <real number> – sets up the scale factor for diagram window main page / /stayontop – project always runs on top / /readonly – project cannot be saved while running / Examples: / 1. Running of a video frame without main window: / "c:\SimInTech\bin\mstarter.exe" /nomainform "C:\SimInTech\Projects\PULTS\10CWA10_L.prt" /nomenu /hidemenus /noborder /top 0 /left 1600 /width 1600 /height 1200 /run