SimInTech Purpose
SimInTech implements the following modes of operation: / MODELING, which ensures: / modeling of non-stationary processes in continuous, discrete and hybrid technical systems including for data interchange (synchronous or asynchronous) available with external programs and devices; / edition of parameters of block diagram and calculations in on-line mode; / real-time calculations or in simulation time zoom mode; / re-start, back-up and display of modeling results. / MONITORING AND CONTROL, which allows: / electronic (virtual) analogs of measuring instruments and control devices to be generated for operational monitoring and control of transient processes in a modeling object; / statical signals processing (including external ones) based on fast Fourier transform to be carried out. / CODE GENERATION, which provides: / automatic generation of a code in C language for one or, when in bulk mode, for several target systems using algorithm schemes typed in SimInTech; / assembly of a designed module, its loading onto a target system, tuning of module (algorithm) execution on an external target system; / automated arrangement of intradevice exchange in case several devices are programmed simultaneously. / ANALYSIS, which provides: / calculations of amplitude-phase frequency characteristics for any linear system and for a majority of non-linear systems (logarithmic gain, phase-frequency characteristic, different hodographs, etc.); / calculation of coefficients, poles and zeros for transfer functions. / OPTIMIZATION, which allows the following tasks to be solved: / parametric optimization of the automatic control system and identification of experimental data; / synthesis of optimal regulators and optimal control in multicriteron setting in case of available restrictions for values of dynamic variables, control actions, parameters of automatic control system elements, performance functionals. / SYNTHESIS, which allows: / regulators with preset characteristics to be synthesized using the frequency and root methods. / Note: presently (May, 2013) modes ANALYSIS, OPTIMIZATION and SYNTHESIS are under internal testing and unavailable for the distributed version of SimInTech.