Water and water steam properties
Mathematical function interpreter and, respectively, “Programming language” block of this version of SimInTech software include 8 special functions to implement determination of basic thermodynamic properties of water and water steam (known Vukalovich tables within the range: for pressure – from 0.09 to 50 MPa and for temperature – from 10 to 800 °С). / Record of these functions appears as follows: / waterps(P,flag); – calculation of properties of water by saturation line pressure; / waterts(T,flag); – calculation of properties of water by saturation line temperature; / steamps(P,flag); – calculation of properties of steam by saturation line pressure; / steamts(Т,flag); – calculation of properties of steam by saturation line temperature; / waterpt(P,T,flag); – calculation of properties of water by pressure and temperature; / waterph(Р,H,flag); – calculation of properties of water by pressure and enthalpy; / steampt(P,T,flag); – calculation of properties of steam by pressure and temperature; / steamph(P,H,flag); – calculation of properties of steam by pressure and enthalpy; / For example, record / v_spec = waterps(1е6,4); / corresponds to calculation of specific volume of water v_spec (flag is equal to 4) on saturation line at pressure of 1·106 Pa (1 MPa). / Values of parameter flag can vary from 1 to 12 and correspond to calculation of the following thermodynamic characteristics of water or water steam: / 1 – pressure; / 2 – temperature; / 3 – enthalpy; / 4 – specific volume; / 5 – Prandtl number; / 6 – dynamic viscosity; / 7 – heat conductivity factor; / 8 – entropy; / 9 – specific heat capacity Cp; / 10 – specific heat capacity Cv; / 11 – derivative density for enthalpy with constant pressure (∂ρ/∂i)P; / 12 – derivative density for pressure with constant volume (∂ρ/∂p)V; / Input parameters and return values of thermodynamic parameters of water or water steam are presented in SI system (except temperature that is measured in °С).