waterps
Special function calculating properties of water by saturation line pressure. Range: for pressure – from 0.09 to 50 MPa and for temperature – from 10 to 800 °С. / Record of the function appears as follows: / waterps(P, flag); / For example, record / v_spec = waterps(1е6,4); / corresponds to calculation of specific volume of water v_spec (flag is equal to 4) on saturation line at pressure of 1·106 Pa (1 MPa). / Values of parameter flag can vary from 1 to 12 and correspond to calculation of the following thermodynamic characteristics of water: / 1 – pressure; / 2 – temperature; / 3 – enthalpy; / 4 – specific volume; / 5 – Prandtl number; / 6 – dynamic viscosity; / 7 – heat conductivity factor; / 8 – entropy; / 9 – specific heat capacity Cp; / 10 – specific heat capacity Cv; / 11 – derivative density for enthalpy with constant pressure (∂ρ/∂i)P; / 12 – derivative density for pressure with constant volume (∂ρ/∂p)V; / Input parameters and return values of thermodynamic parameters of water are presented in SI system (except temperature that is measured in °С).